## Slide 1: Geology, Water Resources Development and Associated Issues in Nigeria
By
Dr OO Yaya (Director, RC-IRBM)
National Water Resources Institute,
Kaduna – Nigeria
@
Inauguration of Ethiope River towards its Adoption as UNESCO Ecohydrology Demonstration Site
On
26th September, 2023

## Slide 2: Order of Presentation
Overview of Geology of Nigeria
Groundwater Occurrence and Distribution
Groundwater Development and Management
Hydraulic connection between Groundwater and Surface Water
Integrated Water resources Management (IWRM)
Integrated River Basin Management (IRBM)
Borehole Siting, Construction and Management
Institutional Framework for Groundwater Development and Management
Ecohydrology for Environmental Sustainability
Water Diplomacy and Conflict Management

## Slide 3: Overview of Geology of Nigeria
ROCK TYPES/CYCLES; ☆Igneous Rocks Those which are formed by the molten rock materials (Magma). e.g. Granite, basalt, dolerite, diorite, gabbro e.t.c. ☆Sedimentary Rocks Those which are produced by the deposition and accumulation of debris transported by rivers, ice, wind e.t.c. e.g. sandstones, limestones, shales, e.t.c. ☆Metamorphic Rocks Those which are formed from the alteration of igneous and sedimentary rocks by heat and pressure. e.g. gneisses, migmatites, slate, marble. e.t.c.
A generalized geological map of Nigeria

## Slide 4
Geology broadly consists of Sedimentary and Crystalline Basement Complex Rocks
Crystalline basement complex rocks dominantly underlay: North Central; South West; and some parts of Eastern flank while sedimentary rocks dominantly underlay: North East; South East; and South-South
Continental Flood Plains define a Y shape on the map with Lokoja in central Nigeria as the confluence point of the international rivers
Geology does not respect human defined or fixed boundaries and transboundary, crossing national and international boundaries.
In the north west, these sedimentary rocks largely consist of Tertiary and Cretaceous rocks of the Sokoto Basin (the south eastern part of the Iullemmeden Basin), which are made up of varying amounts of sandstone and clay, with lesser amounts of limestone

## Slide 8: The Rock Cycle
The rock cycle is a basic concept in geology that describes transitions through geologic time among the three main rock types: sedimentary, metamorphic, and igneous. Plate tectonic activity, along with weathering and erosional processes, are responsible for the continued recycling of rocks.Rock transform in a cyclic pattern, in the course of which rock is created, destroyed and altered through the operation and external processes in the earth. This is referred to as the rock cycle.

## Slide 9
Igneous rock is the rock found when magma cools and gets hardened.

## Slide 11: Groundwater Occurrence, Accumulation and Distribution
What is Groundwater - The rainfall that percolates into the ground and moves downwards into pore spaces in soil and cracks in the rocks below the ground surface and accumulate to become groundwater.
Man can develop groundwater when they dig wells or drill boreholes into the rocks.
Groundwater can appear at the surface as a spring through openings that connect with the aquifer at depth.
When a well is dug or a borehole is drilled, water moves into the hole and rises up to a certain level, called the water table. The rock below the water table is completely saturated
The rock or ground above the water table is called the unsaturated (or vadose) zone. The water table is not always at the same distance below the surface of the ground, but is usually deeper in higher areas of land, and closer to the surface in lower lying areas such as valleys.

## Slide 12: Basement Aquifers
The basement rocks generally form low to moderate productivity aquifers where groundwater flow is concentrated in fractures, and often in a weathered mantle, which can develop in the upper few to tens of metres. Boreholes within basement aquifers are typically drilled to depths of 10–70 m, depending on local conditions. Water quality in these aquifers is generally good
Volcanic rocks also occur in Nigeria, forming low to moderately productive aquifers. Borehole yields are typically less than 3 L/s and may be drilled to depths of around 15 to 50 m.
There are issues with drought causing lowering of groundwater levels, both seasonally in dry seasons, and during longer-term periods of low rainfall. This is particularly an issue for local, low storage basement aquifers, both in the north where rainfall is low and in the south, where rainfall is high.

## Slide 13: Unconsolidated Aquifers
Unconsolidated rocks, which predominantly occur in the coastal Niger Delta Basin and along major river valleys, form high to very high productivity aquifers.
Alluvial aquifers are largely unconfined with shallow water tables and are thickest (15 – 30 m) along the rivers Niger and Benue.
In the Niger Delta Basin, the upper Deltaic Formation is unconsolidated and largely unconfined with a shallow water table (0–10 m below ground level), Benin Formation is partly consolidated largely unconfined (locally confined by lower permeability beds) with a water table typically between 3 and 15 m below ground level, but can be as much as 55 m deep. Aquifers can provide yields from 3 to 60 L/s with borehole depths ranging from 10 to 800 m. Water quality issues include salinity, due to intrusion of sea water, iron, and pollution from human activities, particularly in urban areas.

## Slide 14: Sedimentary Aquifers
Rocks in the lower, more southerly part, of the Benue Basin form moderately productive aquifers where groundwater flow is concentrated in fractures. Borehole yields typically vary from 2 to 8 litres per second (l/s), but can be much higher or lower than this depending on the degree of fracturing and weathering. Aquifers tend to be localized and unconfined, with boreholes ranging from 40 to 150 m deep. Groundwater from these aquifers can be highly mineralized.
Rocks in the Upper Benue Basin typically form low to moderate productivity aquifers, with borehole yields varying between 1 and 5 L/s. Groundwater flow is largely inter-granular and boreholes can vary in depth from 30 to 300 m. Groundwater quality is generally good.[5]
Rocks in the Nupe Basin form low to moderately productive aquifers. Groundwater flow predominantly occurs through pore spaces in the rocks, which are generally fine grained and slightly cemented, limiting groundwater potential. Where coarser sandstones dominate, yields of 2 to 4 L/s can be achieved; basal conglomerate beds may support higher yields.
Borehole yields in rocks of the Sokoto Basin are highly variable, but can be moderate to highly productive where coarser sandstones dominate. Lower sandstones can be confined while upper sandstone layers are typically unconfined.
The Chad Formation, found in the Chad Basin, forms a moderate to highly productive aquifer, with yields up to 30 L/s recorded. Groundwater flow is largely intergranular and aquifers can be unconfined or confined depending on local conditions. Deeper sandstone layers are often confined. The Gombe Formation, also in the Chad Basin, has much lower permeability providing yields of around 1 to 5 L/s. Natural water quality from both these formations is generally good.

## Slide 16
① Unconfined water. ② Aquiclude ③Confined water *Confined water : It is at the deep surface of the earth. *Unconfined water (Free water) :There are many cases that a shallow place has it from the ground level.
evaporation
evaporation
evaporation
shallow well
base rock
Fracture
River
deep well

## Slide 17: Some facts about groundwater in Nigeria
Groundwater is unevenly distributed across the country
Groundwater is widely used for domestic, agricultural and industrial supplies
In 2018, it was estimated that over 60% of its total population depend on groundwater point sources for their domestic supply
73% in rural areas and 45% in urban, with the cities of Port Harcourt, Calabar and Damaturu solely depend on groundwater for their water supply
In 2013, there were around 65,000 boreholes extracting about 6,340.000cubic metre/day, 45,000 of which are hand pumps sustaining supplies for rural and small towns
Estimates of total renewable groundwater resources and groundwater recharge across the country are variable
The FAO estimates that Nigeria has 87,000million cubic metre per year of renewable groundwater
JICA estimates that total annual groundwater recharge to be 155,800million cubic metre per year.
Groundwater recharge is variable across the country and largely controlled by climate: recharge is lower in the north of the country due to higher evapotranspiration low rainfall.
There are local issues of over-abstraction of groundwater, drought, climate change causing lowering of groundwater levels, with no reported cases of land subsidence seasonally in dry seasons, and during longer-term periods of low rainfall. This is particularly an issue for local, low storage basement aquifers, both in the north where rainfall is low and in the south, where rainfall is high.

## Slide 18: Transboundary groundwater
There are several transboundary aquifers in Nigeria:
The Iullemeden, Taoudeni/Tanezrout Aquifer Systems (ITAS), shared by Algeria, Benin, Burkina Faso, Mali, Mauritania, Niger and Nigeria.
The Chad Basin Aquifer, shared by Cameroon, Central African Republic, Chad, Niger and Nigeria.
The Keta Basin Aquifers, shared by Ghana, Togo, Benin and Nigeria.
The Benue Trough, shared by Cameroon and Nigeria
The Rio Del Rey Basin, shared by Cameroon and Nigeria along the coast.

## Slide 19: Groundwater Quality
Groundwater pollution related to human activities (agriculture, domestic waste, industry) are issues in shallow aquifers, particularly permeable unconsolidated deposits, which have little protection from surface activities.
Natural groundwater quality issues have also been recorded. Examples of this include high salinity in shallow alluvial aquifers due to dissolution of evaporate minerals and high iron and manganese concentrations in confined aquifers with low dissolved oxygen (i.e. anaerobic)

## Slide 20
Example of Structured Questionnaire for sourcing information during field reconnaissance

## Slide 21: Ask Local People
Local people who are working for water supply, drilling, well construction and so on are a good source of groundwater information.
These people are experienced and often have a lot of local information on the project area to offer, and they may have very detailed information.
It is also often much easier to speak with local people than it is to find books and reports
Government workers, university experts, local Hydrogeologists, Drillers, NGO workers and Consultants are all sources of information and advice.

## Slide 22: Ask Local People
◆What types of rocks are found under the area, and what are their hydrogeological properties? ◆How many people in the area use groundwater sources such as wells and boreholes for their water supply? If the answer is very few, then why is this? ◆What are the main water supply problems in the area? ◆Do wells and boreholes ever fail (dry up), and if so why is this? What actions do people take when this happens? ◆Have there been any changes over the years in the amount, depth or quality of the groundwater? ◆Are there any water quality problems, which are known? What is the effect of these problems on water users? Does the water make people sick? ◆What is the rainfall for the area, and is anything known about the recharge of groundwater from the surface? The length and quality of rainfall records is important ◆What is the drilling success rate for boreholes in the area? Are all boreholes successful, or are some of them dry? ◆How were the boreholes sites located, and what methods were used to find groundwater in the area? ◆How deep are the boreholes normally? ◆Are there any things which might contaminate groundwater in the area, such as factories, illegal dump sites or sewage pipes? ◆Are there any other people with hydrogeological expertise in the area?

## Slide 23: ◆Rock outcrops, which are often found in river valleys or road cuttings. Take samples, measurements and photographs of the rocks, and try to decide how they fit into the regional geology. ◆Mark the positions of wells and boreholes on a map, and ask local people about the quantity and quality of the groundwater. Test the borehole or well water for conductivity and pH, and if possible take chemical samples for later analysis. ◆Look at and describe the topography of the area. Does it seem to relate to the location of groundwater sources? Perhaps groundwater is found only in valleys ◆Examine any surface water features, which are visible, because these may be dependent upon groundwater, or they may even be a source of groundwater recharge. ◆Look out for any potential sources of contamination such as factories, pipelines and latrines, soak ways (cesspools), unengineered landfills ◆If possible, geophysical investigations using equipment such as a electromagnetic sounding or an electric prospecting can be carried out. This is often best done with reference to satellite images or topographical maps. Any planning of geophysical work should be matched to the geological or hydraulic features to be detected. Geophysics needs specialised equipment and training.
Practical Field Reconnaissance - Here are some things to ask about or look for:
Notes: Geological Map

## Slide 24: The Resistivity Method of Geophysical Investigation for groundwater development
The Electrical Resistivity technique is the longest-established geophysical method used to site wells and boreholes throughout the world. The technique measures the resistance of the ground to electrical currents passing through it.
Resistivity is the inverse of electrical conductivity. The resistance of a geologic medium to current flow when a potential (voltage) difference is applied is
Where R is the resistance, V is the voltage and I is the current. For a given material with a characteristic resistivity, the resistance is proportional to the length of material being measured and inversely proportional to its cross-sectional area.
Where ρ is the characteristic resistivity of the geologic medium, A is the unit cross-sectional area, and L is its length.
=
R
V
I
=
R
ρ L
A

## Slide 25: The theory of operation of D.C resistivity
The figures below are schematic diagrams showing the basic principle of Direct Current (D.C) resistivity measurements. Two short metallic stakes (electrodes) are driven about 1 foot into the earth to apply the current to the ground.
Two additional electrodes are used to measure the earth voltage (or electrical potential) generated by the current.
The depth of investigation is a function of the electrode spacing. The greater the spacing between the outer current electrodes, the deeper the electrical currents will flow in the earth, hence the greater the depth of exploration.
The depth of investigation is generally 20% to 40% of the outer electrode spacing, depending on the earth resistivity structure.

## Slide 26: Some electrode array configuration for carrying out electrical resistivity survey during groundwater investigation
Figures show Wenner, Schlumberger and dipole-dipole arrays from top to the bottom

## Slide 27: Typical survey point and survey line arrangements

## Slide 28: Vertical Electrical Sounding
McOHM, OYO Corporation
STING R1, Advanced Geosciences Inc
SYSCAL R2
ABEM Terrameter SAS300B
Notes: Electrical Soundings

## Slide 29: Theory and Practical operations the electrical resistivity method
Electrode installation
Survey points selection
Watering of electrodes to reduce contact resistance
Electric investigation measurement
Analytic example
Location map
Cross-section
Apparent resistivity profile
Electrode spreading

## Slide 30
The plots below show resistivity distribution of 3 layer structures and appearances of resistivity curves - Rough visualization of structure can be estimated as shown in the figures from the resistivity curves.

## Slide 31: Report writing - Example of georesistivity cross-sections

## Slide 33: Procedures for Groundwater Development through boreholes
Borehole drilling point sited
Mobilization of drilling equipment and accessories
Site preparation (Equipment positioning and digging of mud mixing and cuttings settling pits)
Drilling proper to the required depth using rotary or Down the Hole Hammering or both
Design of the borehole structure
Installation of casings and screens (pVC or steel or stainless steel)
Gravel packing (preferably, river sands and not rock chippings)
Borehole development (by backwashing, overpumping, surging etc)
Grouting of the top annular space with concrete mixture
Pumping test (Step drawdown test, constant discharge test and recovery test)
Water quality tests (Physico-chemical and microbiological examinations using appropriate field protocols for sample collections and accredited laboratory for analyses)
Report writing
Commissioning of the scheme

## Slide 37
Most shallow wells are found in the valley bottom
Water collection mainly by children

## Slide 39: Hydraulic relationship between surface and groundwater
Groundwater and surface water physically overlap at the groundwater/surface water interface through the exchange of water and chemicals.
This exchange is a critical part of the hydrologic cycle. Surface water supplies recharge to the underlying aquifer, where the groundwater can remain in storage for days, months, years, centuries, or even millennia.
Eventually the groundwater discharges back into the stream. Depending on how much time the water spends underground, and the geochemical conditions within the aquifer, the quality of the original recharge water can undergo profound changes before it discharges at the surface
Surface water and groundwater systems are connected in most landscapes. Streams interact with groundwater in three basic ways: streams gain water from inflow of groundwater through the streambed streams lose water by outflow through the streambed or they do both depending upon the location along the stream.

## Slide 40
INTEGRATED WATER RESOURCES MANAGEMENT (IWRM)

## Slide 41: Integrated Water Resources Management (IWRM)
IWRM is a process which promotes the co-ordinated development and management of water, land and related resources, in order to maximize the resultant economic and social welfare in an equitable manner without compromising the sustainability of vital ecosystems

## Slide 43: Challenges and Constraints
Developing appropriate legislative instruments and inadequate enforcement of laws
Setting up institutional management framework in a River Basin requires time and tact
Capacity building within the Local Government Assemblies for effective participation in IWRM is limited and not easy to retain
Public awareness needs to be sustained and requires a lot of financial resources
Establishing cost effective and sustained data collection and monitoring
Ensuring sustained funding for effective implementation of integrated management of water resources plans
Poor attitudes towards the handling of the natural environment
Political interference/manipulation

## Slide 45: Challenges and Constraints (Continuation)
    Climate change and climate variability impacts on water and other natural resources are inadequately described and insufficiently incorporated in sectoral water management strategies
    Many activities in river basins leading to catchment degradation and poor water quality are unregulated
    Inadequate data and information on surface and groundwater quantity as well as quality
    Inadequate skilled human resources for IWRM at all levels
    Inadequate regulations on control of discharge of effluent from industrial and domestic sources
    Systems for early warning and mitigation of effects from floods and droughts are inadequate
    New protocols on the joint management of on shared groundwater resources

## Slide 46: IRBM Key activities
Water Resources Development
Water Resources Management Studies
Master Planning and Policy Development
Investment Planning and Feasibility Studies
Soil erosion assessment and planning of control strategies
Water supply and demand assessment
Water resources system modeling
Environmental Management
Environmental impact assessment
River and floodplain ecology and rehabilitation
Database Management
Database development
Design of decision support systems

## Slide 47
ECOHYDROLOGY FOR ENVIRONMENTAL SUSTAINABILITY

## Slide 48
The world is faced with challenges related to water resources quantity and quality;
Global scenarios suggest that almost two-thirds of the world's population will experience some water stress by 2025 which will accelerate water and environmental degradation to a unimaginable scale;
Consequently, provision of water for societal and environmental needs will no doubt become a major challenge toward achieving sustainable management of water resources.

## Slide 49: Ecohydrology
Under the umbrella of IWRM, Ecohydrology is a subdiscipline of Hydrology, that scientifically produces a series of proven management tools in the field and uses ecosystem processes to achieve the goals of freshwater resource management from a watershed perspective.
Just as Hydrologists must be trained within a multidisciplinary context, so that they acquire the skills and abilities that allow them to participate and lead efforts that search for the solution to environmental problems,
Aquatic ecologists must be adequately trained in hydrological principles, which can be used during all phases of the management of rivers, lakes, and other aquatic ecosystems.
The result will be an ecohydrologist with a holistic vision and systemic thinking, which will allow him or her to develop solutions to the socio-environmental problems related to water.

## Slide 50: About Jabi Lake
Jabi Lake
Jabi Lake is an inland water body located in the heart of Abuja City in Nigeria;
It is a man-made lake that covers a total surface area of about 130 hectares;
The lake was developed for the purpose of water supply to Abuja City but later abandoned;
It is now being used for un-organized fishing and recreational activities.
Source: RC-IRBM, 2020

## Slide 51
Effect of invasive aquatic plants especially on navigation and volume capacity of the lake

## Slide 52: Why EH for Jabi Lake?…

## Slide 53
Harnessing one of the economic potentials of Jabi Lake to empower youth and women
Turning water hyacinth from being a menace to useful household product - A waste to wealth initiative

## Slide 54
TRANSBOUNDARY WATER COOPERATION AND WATER DIPLOMACY

## Slide 55: Cooperation over shared waters
It is currently estimated that 2 billion people rely upon groundwater sourced from transboundary aquifers and 40 per cent of the global population depends on the world’s estimated 310 transboundary river basins.
Despite this, about two-thirds of the world’s transboundary rivers do not have a cooperative management framework, and cooperation on transboundary aquifers is lagging even more.
Cooperation over shared water resources is essential for environmental sustainability, climate change adaptation, regional peace and security, and economic growth. Transboundary water cooperation and water diplomacy processes, which support transboundary water cooperation, can create new opportunities for riparian states to sustainably develop their shared water resources while generating benefits beyond the water sector.
Transboundary water cooperation seeks to establish, enhance, or lay the groundwork for formal or informal water dialogues, institutional arrangements, and/or technical processes for shared water management decision making. It further seeks to improve coordination of diplomatic and development efforts around shared waters.
Water cooperation engage in joint capacity building, experience sharing, knowledge exchange, and skills building activities, supporting development of women water experts in the region and enhanced regional water cooperation

## Slide 56: Goal
Support the effective and equitable allocation and development of water resources, and harmonization of water governance systems by supporting the application of integrated water resources and cooperative river basin management principles to shared water resources.

## Slide 57: Challenge
Stress on the world’s water resources is projected to continue to intensify in the near future and many of the most affected regions are also, in parallel, impacted by political tensions, armed violence, and internal water mismanagement.
Meeting the rising challenges to global water security will increasingly demand that policy makers at all levels improve transboundary water cooperation, develop benefit-sharing opportunities, and negotiate trade-offs among contending interests, risks, and opportunities by harnessing technical, political, and socio-economic knowledge.
Poor partnership support to stakeholders to overcome political, social, and capacity barriers to transboundary water cooperation so as to promote information and experience sharing, collaborative knowledge building, and joint problem solving in regions where water is or could become a source of conflict
Effectively managing transboundary water resources will require strengthening collaboration across states, sectors, and stakeholders at various levels.
Some of the main challenges to transboundary water cooperation are:
Limited trust between riparian communities hindering political will to seek agreements.
Limited understanding of cooperation risks and benefits.
Limited capacity among water management agencies and stakeholder groups.
Limited coordination between donors, and between diplomatic and development efforts.

## Slide 58: APPROACH
Leverage a multi-disciplinary approach to enhance transboundary water cooperation in conflict sensitive basins through:
Applied research and tools: Critical analysis of new trends and approaches to transboundary water management. SWP develops tools and methods, such as water diplomacy, to unpack the development opportunities in a transboundary water setting.
Facilitation of knowledge and experience sharing: Support engagement in transboundary processes with the long-term goal to promote both regional stability and development. Encourages a holistic approach that incorporates relevant sectors.
Promoting the formation of management frameworks for transboundary water: By outlining the incentives and benefits of deepening cooperation between parties sharing transboundary waters, SWP promotes the formation of regional management frameworks.
Building capacity in partner organizations: Develops tailored capacity-building programmes built around innovative knowledge and tools, to better equip decision makers, organizations, and development partners of transboundary waters to work effectively, thereby also supporting improved cooperation in these basins.

## Slide 59
THANKS YOU FOR LISTENING